## Slide 1
Little Fool(付康为)
6LoWPAN
The Wireless Sensor Networks of the new generation

## Slide 2
ANIMATIONS

15%
AWESOME WORK
What is 6LoWPAN?
6LoWPAN is a kind of Wireless LAN(Local Area Network).
It is based on IPv6 and IEEE 802.15.4.
It can be used by Low-Power embedded equipments.
6LoWPAN will be promising in IOT field.

## Slide 3
6LoWPAN Framework
6LoWPAN Framework
TCP/IP Framework
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
from “6LoWPAN: The Wireless Embedded Internet”

## Slide 4
ANIMATIONS

15%
AWESOME WORK
6LoWPAN Application
Every node is used for the monitor of the environment.
Border Router is used for the connection between Ethernet and 6LoWPAN WSN.
Users have access to the nodes by their smart phone or PC.

## Slide 5
ANIMATIONS

15%
AWESOME WORK
6LoWPAN vs ZigBee
ZigBee
Similarities
Based on IEEE 802.15.4
Supported by embedded devices
They can both form wireless sensor network.
Differences
zigbee needs routers to transfer the data form end devices.
In 6LoWPAN, every node plays a role as a router.
6LoWPAN has a great compatibility with Internet

## Slide 6
ANIMATIONS

15%
AWESOME WORK
Border Router
Transfer IPv6 packets between Ethernet and 6LoWPAN.
In Ethernet, IPv6 packets are based on IEEE 802.3.
In 6LoWPAN WSN, they're based on IEEE 802.15.4.
Ethernet
6LoWPAN

## Slide 7
ANIMATIONS

15%
AWESOME WORK
Node Design - Hardware
CC2530 has an advantage of power consumption.
Use DS18B20 or DHT11 as Sensors.
Battery supplies power for the whole node.
Relay can turn on or off some devices. It plays a role as a switch.

## Slide 8
ANIMATIONS

15%
AWESOME WORK
Node Design - Software
The node uses Contiki as its runtime environment.
Open source, great portability …
uip6 network protocol stack, 6LoWPAN WSN protocol stack, COAP, MQTT application.
We choose COAP as the application of these nodes.

## Slide 9
ANIMATIONS

15%
AWESOME WORK
COAP Protocol
Constrained Application Protocol
Based on UDP and REST structure
Size of the minimum data packet: 4 bytes
Method: GET, POST, PUT and DELETE
Similar with HTTP
COAP vs. HTTP
coap://machine.address:5683/sensors/temperature
URL example

## Slide 10
ANIMATIONS

15%
AWESOME WORK
Border Router Design
Border Router uses openWRT which is a special embedded linux system.
CC2530 uses its uart to communicate with openWRT system.
The protocol between CC2530 and openWRT is SLIP.
SLIP is a simple Internet protocol that is based on serial line.

## Slide 11

System Testing
Node on the left, Border router on the right
The “ping” test
Border Router: openWRT and CC2530, connected by serial port line.
The node is set as a coap server.
Use command “ping” to test whether the node was connected with the Internet.

## Slide 12

System Testing
coap server test
Use libcoap as the client of the coap server.
“-m get” makes libcoap use GET method to send requests to the coap server.
The function of the coap server is response the simple string for what you request.

## Slide 13
THANK YOU